| INTERNATIONAL TELECOMMUNICATION UNION |  |
| --- | --- |
|  | RRC-04 | REGIONAL BROADCASTING CONFERENCE (FIRST SESSION) | Addendum 11(Rev.1) to Document 7-E |
|  |  |  | 16 January 2004 |
|  |  |  | Original: English/ French/ Spanish |
| GENEVA, 10 – 28 MAY 2004 |  |
|  | PLENARY MEETING |
| EUROPEAN COMMON PROPOSAL FOR THE WORK OF THE CONFERENCE |
| part 11 |

Channel bandwidth and channelling plan for T-DAB
in Band III

Agenda item of Resolution 1185 (modified, 2003) of the ITU Council: resolves 2.1 a).

Introduction

The channel bandwidth is the nominal RF bandwidth of the T-DAB channel, usually called a frequency block. The channelling plan is the frequency block distribution throughout Band III. For T-DAB, the nominal channel bandwidth is 1.75 MHz. The channelling plan for T-DAB is a subdivision of the 7 MHz analogue television channel spacing for System B.

Proposal

EUR/7A11/1

For T-DAB, the channelling plan in Band III as given in Recommendation ITU-R BS.1660 “Technical Basis for planning of terrestrial digital sound broadcasting in the VHF band” should be inserted in the new digital Plan.

Reasons:	A unique channelling plan is frequency efficient.

The T-DAB system has been introduced in many European countries with this channelling plan.

________